## Slide 1: Fluorescence Theory and Fundamentals of Getting Great Data
by Sherry L. Hemmingsen, Ph.D. Molecular Spectroscopy Product Specialist

## Slide 2
JASCO Corporation
JASCO Corporation
Hachioji, Tokyo
Since 1958
JASCO, Inc
Easton, MD

## Slide 3
JASCO: Our Products

## Slide 4: JASCO: > 50 Years in Fluorescence

## Slide 5: Seminar Overview
Fluorescence Theory
  Electronic transitions and processes of deactivation
  Characteristics of fluorescent molecules
  Factors that affect fluorescence intensity
Sample, solution, and quantitative considerations
Instrument design and components, and data collection
Practical Pointers for optimizing fluorescence signal
  Parameter control
  Identifying and minimizing scattering artifacts
  Inner-filtering effects

## Slide 6: Luminescence Theory
Tm = 63 oC

## Slide 7: Fluorescence Applications
Biochemical
  Protein folding, drug delivery, binding interactions, aggregation, imaging
Environmental
  Pollutant detection / tracking, microbial water testing
Materials Science
  Nanoparticles-quantum dots, new material development
Food Science
  Ingredient quantitation, antioxidant testing, packaging
And the list goes on…..

## Slide 8: Types of Luminescence

## Slide 9: How Species Get Rid of Excess Energy
Radiant vs. Nonradiant Energy Loss
Radiative Deactivation:
  Emission of excess energy as a photon (UV-Vis, NIR)
  Luminescence
Nonradiative Deactivation:
  Loss of excess energy without a photon, usually as heat (IR)
  Molecular motion

## Slide 10: Types of Emission Processes
Photoluminescence: Excitation by absorption of light
Fluorescence ns time regime (lifetime 10-11 to 10-7 secs)
Phosphorescence (lifetime 10-3 to 102 secs)
Excitation light source required
Chemi-luminescence: Excitation by chemical reaction
Bio-luminescence: chemiluminescence in a biological system
NO external light required

## Slide 11: Photoluminescence Processes: Fluorescence
ISC
ISC = InterSystem Crossing

## Slide 12: Photoluminescence Processes: Phosphorescence
Paired electron spins
Unpaired electron spins
ISC
ISC = InterSystem Crossing

## Slide 13: What Kinds of Substances Fluoresce?
Highly conjugated organic systems (many alternating single and double bonds)
Aromatic molecules
Rigid, planar molecules

## Slide 14: Highly Conjugated Systems
By NEUROtiker - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=2330317
Beta Carotene

## Slide 15: Aromatic Molecules
Tyrosine
Tryptophan
Phenylalanine
Aromatic amino acids provide intrinsic fluorescent probes for studying protein interactions

## Slide 16: Rigid, Planar Molecules
Polycyclic Aromatic Hydrocarbons or PAHs
(aka, molecular chicken wire) are highly fluorescent

## Slide 17: Your turn….Which molecule fluoresces more?
Biphenyl
Fluorene

## Slide 18: How Fluorescent is a Molecule?
Quantum Yield (Quantum Efficiency)
FF = # photons emitted as fluorescence
# photons absorbed
values range from 0-1

## Slide 19: Your turn…. Which molecule is has the greater quantum efficiency?
1
2
Fluorescein
Phenolphthalein
FF = 0.90
FF << 0.01

## Slide 20: What Factors Affect Fluorescence?
Solution Conditions
  Solvent
  pH
  Ionic Strength
  Temperature
  Concentration
SOOOOOOOO……
Fluorescence is a highly sensitive tool, especially to local microenvironments around the fluorophore
This Photo by Unknown Author is licensed under CC BY-NC-ND
This Photo by Unknown Author is licensed under CC BY-SA
BUT, this requires careful experimental controls…

## Slide 21: Concentration Effects: “low” [ ]’s
F = 2.303 K Io ebc ONLY when 2.303 ebc (= A) < 0.05
K = constant based on instrument geometry
Io = intensity of excitation light
b = pathlength of cell
e = molar absorptivity of fluorophore
c = concentration of fluorescent analyte

## Slide 22: Factors that Increase Fluorescence
Based on the Beer-Lambert equation:
  Intensity of excitation light
  Different from UV!!!
  Molar Absorptivity of Fluorophore
  Concentration of Fluorophore
    Up to a point before other effects take over…

## Slide 23: Take-Home Message 1: Solution and Sample Considerations
Control of solution parameters, fluorophore selection, and sample preparation are the first steps for:
Optimizing your fluorescence measurement
  What is quantum yield of fluorescent probe?
  Where does probe excite and emit?
  Is there background fluorescence in sample or solutions used?
Being confident that the observed changes in fluorescence are due to the experimental parameter that was perturbed.
  Which solution parameters need to be controlled and which do not?
  How consistent is sample preparation?
  Are reagents spectroscopic grade? High water quality?

## Slide 24
Most of you have used a UV-Vis instrument to collect an absorption spectrum.
How many have used a fluorometer?

## Slide 25: What about instrument control? Let’s build a simple fluorometer together.

## Slide 26: Fluorescence spectrophotometer

excitation

emission
Light source
Sample
Light detector
Ex Monochromator
Em Monochromator
Xenon Lamp:
Continuous or Flash
PMT, Photomultiplier Tube
Light detector
Notes: 2 Scanning monochromators
-Fix excitation, scan emission
Fix emission, scan excitation
-scan both

## Slide 27
Absorption, Excitation, and Emission Spectra
Absorption spectra are often, but not always the same as excitation spectra
Emission is at longer wavelengths than excitation
Stokes Shift = difference between excitation and emission maxima
Phosphorescence is much weaker than fluorescence
Phosphorescence has a MUCH greater Stokes Shift than fluorescence.
Absorption and Excitation

## Slide 28: Excitation Scan
Light source

excitation

emission
Sample
Detector
Monochromator
Monochromator
  Fix emission monochromator and
  scan excitation monochromator
  Result is
  A fluorescence excitation spectrum

## Slide 29: Emission Scan

excitation

emission
Sample
Detector
Monochromator
Monochromator
Light source
  Fix excitation monochromator and scan emission monochromator
  Result is the fluorescence emission spectrum

## Slide 30: What information can we get from an Emission spectrum?
Information on molecular structure and fluorescent moieties
Local environment surrounding molecule being probed
Usually, the shape of the fluorescence spectrum is independent of the excitation wavelength
Emission spectrum is often a “mirror image” of the excitation spectrum

## Slide 31: Fluorescence of Anthracene
Excitation
Emission

## Slide 32: Scattering Artifacts in a Fluorescence Spectrum
Fluorescence or Scatter…how can you tell?

## Slide 33: Types of Scatter
RAYLEIGH
elastic scattering
energy of scattered light = energy of excitation
RAMAN
inelastic scattering due to solvent
energy of scattered light < energy of excitation

## Slide 34: Identifying Rayleigh vs. Raman Scattering
RAYLEIGH (1st and 2nd Order)
If lscatter = lex 1st order
If lscatter = 2lex 2nd order
Most apparent in solids and highly scattering solutions
RAMAN
If lscatter > lex
Raman
EASY TO IDENTIFY RAYLEIGH!
But fluorescence is also > lex …Right???

## Slide 35: Identifying Fluorescence vs. Raman (in solution)
Qualitative Method
Observed peak is likely Raman if:
Peak shifts to longer l as the lex is increased
Peak also appears in the spectrum of the blank
Run emission scans at different lex for both sample and blank!

## Slide 36: Identifying Fluorescence vs. Raman (in solution)
Quantitative Method
Calculate the Raman band for the solvent at the lex used
For water:
lRAMAN = lex / (1 – 3.39 x 10-4 lex)
If lex = 300 nm then lRAMAN (in water) = 335 nm
If lex = 350 nm then lRAMAN (in water) = 397 nm
(The 3.39 x 10-4 nm-1 is a the Raman shift specific to water…use 2.92 x 10 -4 and 1.43 x 10 -4 for ethanol, 2.87 x 10 -4 for cyclohexane).

## Slide 37: Optimizing Fluorescence: Examples in Spectra

## Slide 38: Scatter in Water lEx = 300 nm
300 nm
335 nm
RAYLEIGH
SCATTER
l = lEx
RAMAN
l > lEx

## Slide 39: Cranberry Juice: Diluted lEx = 365 nm
365 nm
730 nm
450 nm
RAYLEIGH
SCATTER
l = lEx
2nd ORDER RAYLEIGH
SCATTER
l = 2lEx
RAMAN or FLUORESCENCE??
l > lEx

## Slide 40: Cranberry Juice: Decreasing lEx
Moving lEx to shorter l
Shifts band to shorter l
lEx = 365 nm
lEx = 350 nm
lEx = 330 nm

## Slide 41: Cranberry Juice: Fluorescence?
lEx = 365 nm
lEx = 350 nm
lEx = 330 nm
Band at 450 nm only changes in intensity
Must be fluorescence!
Band at shorter ls shifts with D in lEx
Must be Raman!
450 nm
??

## Slide 42: Instrument Parameters
Slits / SBW
Detector HV
Internal Filters
lEx , lEm

## Slide 43: Cranberry Juice: Different Spectral Bandwidths (SBW)
SBW F
10 nm 7800
5 nm 800
2.5 nm 51

## Slide 44: Cranberry Juice: 5nm SBW at Different Detector Voltages
Detector F
550 V 8000
500 V 4000
400 V 800

## Slide 45: Spectral Bandwidth and Resolution
SBW
10 nm
5 nm
2.5 nm
Ovalene
SBW Resolution

## Slide 46: Quantitative Fluorescence and Inner Filtering Effects

## Slide 47: Which one has the greatest fluorescence signal?

## Slide 48: Which one has the greatest fluorescence signal?
F
Concentration

## Slide 49: Concentration Effects: High [ ]’s
Self (concentration) quenching
Formation of new species after absorption
Energy transfer
Inner filtering effects
Factors which F as c:
Recall from F = 2.303 K Io ebc

## Slide 50: Excitation in a Cuvette: A View from Above
EX
EM

## Slide 51: Typical Fluorescence: A Cuvette View
Green Excitation
penetrates all the way across cuvette
Red Fluorescence is seen across entire
emission face
NO INNER FILTERING!!!
EX
EM

## Slide 52: Primary Inner Filtering View In a Cuvette
EX
EM

## Slide 53: Inner Filtering: A Cuvette View Primary Absorption
Green excitation light does not penetrate
across the full width of the cuvette.
More concentrated solution BUT
much less fluorescence because
most of molecules are not excited.
PRIMARY ABSORPTION occurs before the
emission of a photon of light.
EX
EM

## Slide 54: Inner Filtering: A Cuvette View Secondary Absorption
Some of the shorter emitted l’s are reabsorbed
Emission signal is attenuated at shorter wavelengths
which produces an apparent red shift
SECONDARY ABSORPTION results from
overlap of lex and lem for the fluorophore
Occurs in fluorophores with a narrow Stokes Shift
EX
EM

## Slide 55: How to Minimize Inner Filtering
  Use more dilute solutions
    Try to work in linear range!
    Keep Abs < 0.005 at maxima for both lex and lem
  Try a shorter pathlength cuvette
  Use front face illumination (triangular cells)

## Slide 56: Take-Home Message 2: Parameters for Fluorescence Optimization
Careful compromise of instrument settings for best signal:
  Wavelength Selection for lEx and lEm
  Exclude scatter to maximize sample signal
  Identify and move Raman band way from peaks of interest
  Filters for excitation and emission channels
  USE filters to minimize 2nd order scatter
  May need additional external filters
  PMT detector sensitivity (V)
  Find detector voltage V that enhances signal with least noise
  Slit Widths or Spectral Bandwidth (SBW)
  Find SBW that provides desired combination of
    signal and resolution, minimizing noise
  RULE of THUMB:
  sum SBW for ex/em slits < Stokes Shift (lEm – lEx)

## Slide 57: Thanks for joining us!! Questions?

## Slide 58: JASCO Educational Resources
Upcoming Webinars:
  Circular Dichroism
  Vibrational Circular Dichroism
  FTIR Theory, Instrumentation, and Techniques
  FTIR Microscopy
  Raman Microscopy and Imaging
  SFC Theory and Applications
E-books and/or Tips and Tricks Posters
  Raman
  Fluorescence
  FTIR
  CD
KnowledgeBase
NEXT WEBINAR WILL BE ON
CD THEORY AND APPLICATIONS
DR. LEAH PANDISCIA
TUESDAY APRIL 14TH AT 2:00 PM EDT